## Slide 1: Network-Accelerated Distributed Deep Learning
Omar Alama | Marco Canini | Jiawei Fei
Chen-Yu Ho | Jacob Nelson | Amedeo Sapio

## Slide 2: Agenda
Session I
Distributed DNN training overview
When the network is the bottleneck
SwitchML: In-network aggregation
SwitchML hands-on
  Training with SwitchML
  SwitchML API
Session II
OmniReduce: Sparse collective communication
OmniReduce hands-on
GRACE: Gradient compression
GRACE hands-on
  Implement and run a gradient compression algorithm

## Slide 3: Agenda
Session I
Distributed DNN training overview
When the network is the bottleneck
SwitchML: In-network aggregation
SwitchML hands-on
  Training with SwitchML
  SwitchML API
Session II
OmniReduce: Sparse collective communication
OmniReduce hands-on
GRACE: Gradient compression
GRACE hands-on
  Implement and run a gradient compression algorithm

## Slide 4: Deep Learning
Increasingly sophisticated models
Increasingly larger datasets
Innovation fueled by leaps in (costly) infrastructure:
Clusters with hundreds of machines, each with many HW accelerators (GPUs, TPUs, etc.)
Compute requirements doubling every 3 months!
Training models is still very time-consuming: days or even weeks!
Notes: Modern ML solutions are so successful because they can build increasingly sophisticated models to accurately represent real world problems, and, as models become more complex, they require training on increasingly larger datasets.
This increase in size and complexity made distributed training very common. With distributed training, large-scale clusters use hundreds of nodes to run training jobs, and each node can be equipped with multiple hardware accelerators. Nevertheless, a training job can still take many hours, days or even weeks.

## Slide 5: DNN training
Layer 1
Layer 2
Layer 3
DNN model
Minibatch
ℒ
Loss
Forward pass
Backward pass
Stochastic gradient descent
SGD:
iterative algorithm to train model parameters
stochastic gradient at iteration

## Slide 6: Data-parallel distributed DNN training
ℒ
W1
Layer 1
Layer 2
Layer 3
ℒ
W2
Layer 1
Layer 2
Layer 3
ℒ
W3
Layer 1
Layer 2
Layer 3
ℒ
W4
Layer 1
Layer 2
Layer 3
Data samples

## Slide 7: Compute-communication overlap
ℒ
W1
Layer 1
Layer 2
Layer 3
Time
1
2
3
3
2
1
3
2
1
Gradient synchronization
Wait on the network
Next iteration starts
1

## Slide 8: Data-parallel distributed DNN training
Data samples
W1
W3
W2
W4
Gradient synchronization
All-to-all intensive communication pattern

## Slide 9: All-to-all reduction
Data samples
W1
W3
W2
W4
Gradient synchronization
+

## Slide 10: All-to-all reduction
Data samples
W1
W3
W2
W4
Gradient synchronization
+
+
+

## Slide 11: All-to-all reduction
Data samples
W1
W3
W2
W4
Gradient synchronization
+
+
+
=

## Slide 12: All-to-all reduction
Data samples
W1
W3
W2
W4
Gradient synchronization
+

## Slide 13: AllReduce
Data samples
W1
W3
W2
W4
Gradient synchronization
Form a logical ring (or tree, etc.) and run peer-to-peer communication

## Slide 14: Parameter server (PS)
Data samples
W1
W3
W2
W4
PS
Push gradients
Aggregate updates at PS
Pull aggregated gradients
  (or updated model parameters)

## Slide 15: The network bottleneck
When is the network a bottleneck?
  1st order: The ratio of communication to computation
  2nd order: The non-overlappable communication
DeepLight training – 1 iteration
Time (ms)
Overlap
see Section 2.2 of SwitchML paper [NSDI ’21]
No overlap

## Slide 16: The network bottleneck
Compute accelerators performance improvements have so far outpaced network bandwidth increases
Newer, larger DNN models spend more time on communication
Chart: Profile of benchmark DNNs (10Gbps)
| SSD | ResNet-50 | UGATIT | VGG19 | BERT | NCF | LSTM | DeepLight
Communication | 0.26 | 0.29 | 0.28 | 0.73 | 0.67 | 0.72 | 0.94 | 0.97
Overlapping communication | 0.2574 | 0.1943 | 0.2352 | 0.4891 | 0.0201 | 0.0288 | 0.094 | 0.0194
Chart: Profile of benchmark DNNs (100Gbps)
| SSD | ResNet-50 | UGATIT | VGG19 | BERT | NCF | LSTM | DeepLight
Communication | 0.03 | 0.03 | 0.04 | 0.1 | 0.17 | 0.23 | 0.46 | 0.79
Overlapping communication | 0.0297 | 0.0282 | 0.0396 | 0.099 | 0.0595 | 0.0621 | 0.2576 | 0.158

## Slide 17: The network bottleneck: hypothetical scaling
Faster GPU that leads to contiguous network saturation at 100 Gbps
  (considering measured non-overlappable communication)
Chart: Network-saturating computation scaling factor
| SSD | ResNet-50 | UGATIT | VGG19 | BERT | NCF | LSTM | DeepLight
 | 15.2 | 19.8 | 17.6 | 6.7 | 3.5 | 1.2 | 1.5 | 1

## Slide 18: Questions?

## Slide 19: First hands-on
Goal: Run your first distributed DNN training job with TF + Horovod
Horovod what?
  Horovod is a distributed DL toolkit with a simple API
  Does worker coordination and leverages NCCL, MPI or Gloo collectives
Will now train a simple MNIST classifier. Expect to see something like:
opt = hvd.DistributedOptimizer(opt, ...) # Wrap the optimizer
[1,0]<stderr>:I0827 10:26:35.182926 140002329507648 basic_session_run_hooks.py:260] loss = 0.04415287, step = 90 (0.765 sec)
[1,1]<stderr>:INFO:tensorflow:loss = 0.045447636, step = 90 (0.764 sec)
[1,1]<stderr>:I0827 10:26:35.182554 139970903414592 basic_session_run_hooks.py:260] loss = 0.045447636, step = 90 (0.764 sec)
[1,0]<stderr>:INFO:tensorflow:loss = 0.055977736, step = 100 (0.776 sec)
[1,0]<stderr>:I0827 10:26:35.958616 140002329507648 basic_session_run_hooks.py:260] loss = 0.055977736, step = 100 (0.776 sec)
[1,1]<stderr>:INFO:tensorflow:loss = 0.05445839, step = 100 (0.775 sec)
[1,1]<stderr>:I0827 10:26:35.957948 139970903414592 basic_session_run_hooks.py:260] loss = 0.05445839, step = 100 (0.775 sec)

## Slide 20: Setup and instructions
Detailed instructions go to https://hackmd.io/@chenyuho/rknwow7WF
Will run on actual K80 GPU instances on AWS – 2 VMs per participant (up to our resource limit)
Acquire a pair of FREE VMs by filling in your name
  mind conflicts – try to spread out in the sheet
Download the net-accel-dl-tutorial.pem SSH private key from Slack channel
  ensure right perms (chmod 0400)
SSH to Primary IP and run the job
  ssh –i net-accel-dl-tutorial.pem ubuntu@$PRIMARY_IP
  ~/scripts/1_tf_mnist.sh
All working well? Open the script ~/scripts/tensorflow_mnist.py
  Can you identify the Horovod code?